## Slide 1
Management of Runaway Risk NR/L2/OHS/019 Module 05
Technical Brief 2021
Compliance date: 6th March 2021
Notes: Keep font size and colour uniform throughout the presentation
Keep PRB Logo in top right
Add the client logo in bottom right if required

## Slide 2
This is a technical briefing issued by Network Rail regarding the risk of ‘runaway’ plant.
This briefing MUST be provided to all Sentinel Card holders on or before 1st March 2021
Ensure all Sentinel Cardholders sign the briefing record once they have received this briefing
Notes: Keep font size and colour uniform throughout the presentation
Keep PRB Logo in top right
Add the client logo in bottom right if required

## Slide 3: Management Of Runaway Risk
Following the Tebay accident on 15 February 2004, and the subsequent ORR requirements for Network Rail to improve the arrangements for dealing with runaway risk, Network Rail and the Trade Unions agreed to work together on a workstream focussed on the potential risk of runaways by Rail Mounted Plant.
Network Rail and the Trade Unions discussed and agreed a formal hierarchy of controls that would eliminate or reduce the risks associated with runaways in possessions. The arrangements are now to be included as a supporting module 05 to the NR/L2/OHS/019 standard
Notes: Main text body to be font size 20
Text colour to be consistent throughout the presentaiton

## Slide 4: Management Of Runaway Risk
Module 05 aligns with section 9.2 of the current NR/L2/OHS/019 standard, and includes:
Additional definitions relating to runaway risk
Responsibilities and actions of those that create the risk
Responsibilities and actions of those that are exposed to the risk
Hierarchy of control measures to remove or reduce the risk, included in a flowchart format
Appointed Watchman and the limitations placed upon the deployment of a watchman.

## Slide 5: Management Of Runaway Risk
Runaway Rail mounted plant Watchman | See the definitions in NR/L2/OHS/019. The following definitions apply to module 05 only: The unauthorised and uncontrolled movement of Rail Mounted Plant. Any plant that has rail wheels or runners that can run on the track either self-propelled or manually propelled. This includes on track machines, on track plant, trolleys, skates, scooters, etc. (as per NR/L2/RMVP/0200) Person appointed to warn of an approaching runaway

## Slide 6: Management Of Runaway Risk
Locations with specific runaway risks
A site of work is deemed at risk from runaways where rail mounted plant is to be used and the following conditions apply:
the site of work is on a gradient steeper than 1 in 100 or has a gradient steeper than 1 in 100 within 5 miles of the site of work;
the site of work is in a possession; and
work is taking place on or near the line.
Note: The requirement for the site of work to be static has been removed as both static and moving sites are equally at risk from potential runaways

## Slide 7: Management Of Runaway Risk
1. | Eliminate the risk by re‐planning the work to be carried out at another opportunity where the risk to others no longer exists.
2. | Isolate the risk by creating a barrier that prevents the runaway from leaving the site of work e.g. a rail removed as part of the work activity.
3. | Set points to isolate the pathway of the equipment causing the risk and restrict its ability to enter another site uncontrolled. When using this as a control, confirm it does not introduce risk to other work groups.
4. | Manage the risk by compliance to GE/RT 8000 Handbook 10 ‐ Duties of the COSS or SWL and person in charge when using a hand trolley, and NR/L2/RMVP/0200 ‐ Infrastructure Plant Manual. If assistance is required to determine compliance requirements, seek advice from the On-Track Plant Specialist or organisational equivalent.

## Slide 8: Management Of Runaway Risk
1. | Eliminate the risk by re‐planning the work to be carried out at another opportunity where the risk to others no longer exists.
2. | Identify if the work activity has created a barrier that prevents the runaway from entering the site of work (e.g. where a rail has been removed as part of the work activity).
3. | Set points to isolate the pathway of the equipment causing the risk and restrict its ability to enter the site of work uncontrolled. When using this as a control, confirm it does not introduce risk to other work groups e.g. where the point setting cannot be maintained.
4. | Implement a Secondary warning system by use of an approved system at the site of work of the potential at risk work groups. Where there is more than one potential ‘at risk’ work group, arrangements can be agreed between responsible managers, planners and persons in charge for one secondary warning system to be deployed at the initial at-risk site, and supplementary warning systems between workgroups can be agreed.
5. | Use of an appointed watchman who cannot be involved in the work activity.

## Slide 9: Management Of Runaway Risk
Appointed watchman
The watchman role is a capability not a competence. When deploying a watchman the following shall be applied:
the watchman shall be identified as a method of warning during the planning stage and the details shall be added to the SSOWPS controls measures box;
the watchman shall be appointed by the PIC or COSS (if delegated COSS duties);
the watchman shall be placed and remain in a position of safety;
the watchman shall have Lookout competence;
the watchman shall not be deployed during darkness, poor visibility or in a tunnel;
the watchman shall have a sighting distance of 500yds/460m minimum;
the watchman shall not be involved in the work;
the watchman shall be close enough to the group to confirm all staff receive warnings;
the watchman shall have sight of all staff to be warned at all times;
where noise is involved the COSS or PIC shall use the touch warning method;
the watchman shall have a whistle or horn (Ideally they should carry both)
if the watchman cannot maintain the agreed sighting distance/visibility, or needs to stand down, they shall inform the PIC/COSS and warn personnel to move to a position of safety;
watchmen shall be rotated from duty every two hours with a 20-minute break before reassuming duty.

## Slide 10: Management Of Runaway Risk
If you have questions or queries regarding the information contained with this briefing please contact us on:
01323 887186,
or email info@prb-consulting.co.uk

## Slide 11: Management Of Runaway Risk
Briefing Record
NAME | DATE | SENTINEL NUMBER | SIGNATURE